## Slide 1: New Outlook on Multi-Domain and Multi-Layer Traffic Engineering
Adrian Farrel afarrel@juniper.net adrian@olddog.co.uk
AUSNOG, Sydney, September 2013

## Slide 2: WHY Do We Care about Multi-Layer Networks?
What is a layer?
  Most obvious definition is technology layers
    Packet-over-optical is seeing a resurgence of interest
    MPLS-over-MPLS is layering
    There are also sub-layers of optical technologies
Routers are connected together
  Hope that is not a shock to you
  Router inter-connect does not need to be a p2p link
    Mesh transport networks offer ways provide variable connectivity and maximise return from a set of transport resources
Many network services are examples of layering
  VPNs are best example
  Pseudowires count as well

## Slide 3: What Problems Are We Trying to Solve?
We need to make connectivity requests from a client network to a server network
  Typically the client cannot see / understand the server topology
  Client networks / nodes typically multi-homed to a server network
  Client networks may be connected to multiple server networks
  Client needs to understand client-layer reachability across the server networks
  Server-layer connectivity may be through a concatenation of server networks

## Slide 4: Some Old Views of Layering
User to Network Interface
  No routing exchange
  No hints about resolving dual homing
  No hints about client layer reachability
Protocol solutions from ITU-T, OIF, and IETF
UNI request is a stab in the dark
UNI

## Slide 5: Flooding Would Be Crazy
Well, it would, wouldn’t it?
Flooding means…
  Telling the client network about all of the links and nodes in the server network
    A shared IGP
    Two IGP instances
    GMPLS actually supports this
Networks usually under different administrations
Scaling is a real concern
It can get messy with multiple server networks
Client network will not understand server links
  All those optical parameters etc.
  Really don’t want to try to send packets down optical links

## Slide 6: Link Aggregation Doesn’t Quite Do The Job
Disadvantages of link aggregation
Waste of transport resources
  Under-use of dedicated resources
n2 scaling issues (full mesh)
  Complexity of server layer planning and management
  Edge nodes need more server layer resources (line cards, lasers, etc.)
Client has no idea of physical path
  Cost of client services is high
  Protection may not be real
Need for frequent advertisement updates
  Every time resource is used on a component path
Computationally expensive to aggregate
  Multiple paths
  Multiple constraints
Advantages of link aggregation
Direct, any-to-any connectivity
Minimize delay in provisioning new client services
Server layer treated as a set of logical links
  No worries about client connectivity
  Simplified client network management
Redundant connections in case of failure

## Slide 7: Node Aggregation Doesn’t Cut it Either
Disadvantages of aggregation
No consideration of path properties
No visibility into disjoint paths
Limited cross-connect ability is hidden
  In particular when network is partitioned
  Issues with wavelength continuity
There are ways to handle limited cross-connects in GMPLS advertisements, but higher layer network will not understand them
Advantages of Aggregation
Very simple model
Scales well
Does not need frequent updates

## Slide 8: How PCE addressed the problem
A
L
M
K
J
I
H
G
E
F
C
B
D
VNT Manager
PCE
A PCE for each network
  Hides topology of one network from the other network
Higher layer PCE reports absent connectivity in higher layer to Virtual Network Topology Manager
VNTM consults lower layer PCE and then provisions connectivity
PCE

## Slide 9: Perhaps the Client Can be in Both Networks
This is a variation of the UNI model
  The UNI is within the node
Only the edge nodes need to be aware of the core network
  The edge node can make choices about the path across the server network
  The edge node could determine potential connectivity and advertise as potential links in the client network
But…
  It doesn’t help planning end-to-end paths
  The edge node (probably a router) needs to be aware of
    All server technologies
    Complex TE parameters (such as optical constraints)
    All vendor-specific issues in the server network
UNI

## Slide 10: Two Unasked Questions
Do we *really* want provisioning in the server layer auto-triggered by activity in the client layer?
  Server may be 100G lambda
  Client may be a UDP packet
  There may be commercial implications
When can I start to send data using the virtual link?
  Many optical circuits need tuning and testing first

## Slide 11: Abstract Links
A virtual link is a link created out of a server-layer LSP.
  Advertised into the client-layer IGP just like any other link
An abstract link is the possibility of a virtual link.
  It is a link that would be formed if an LSP was set up to support it.
  Installed in the client-layer Traffic Engineering Database
    Maybe by IGP or by BGP-LS
Policy is used to determine which abstract links to advertise
  I.e. not all potential links
  Allows stability of selection without frequent re-compute / re-advertisement
  Just key reachability with basic constraints
  Allows knowledge of server network resources, topology, constraints, etc. to be hidden from client
Client layer can see what links might be established
  Ask for them to be turned up if needed
  Reachability is known within the client layer
Abstract converted to virtual link as service request from client layer
  LSP is set up (and tuned and tested)
  Link is advertised into client IGP

## Slide 12: Introducing a Connectivity Layer
IGP in Server Layer
Node Y determines abstract XY
  It’s a policy thing
IGP in Connectivity Layer
  Consists of “Access Links” and “Abstract Links”
  Update “abstract” to “real” when server LSP set up by NMS action
Node V determines abstract VW
IGP in Client Layer
  Consists of normal “Client Links” and “Abstract Links”
  Update “abstract” to “real” when client LSP set up by NMS action
Client
Connectivity Layer
Server
X
V
W
Y

## Slide 13: General Applicability To The VPN
It’s a layered network
It has multi-homing and reachability issues
We need to provision TE connectivity
Discussion is about better VPN enablement for the carrier

## Slide 14: Applicability to Peer Domains
Strong driver for tier 1 VPN providers
Need to leak “TE reachability” without flooding mega-data
Key components are
  Abstract links
  Connectivity Layer
  BGP-LS
  PCE

## Slide 15: draft-farrel-interconnected-te-info-exchange Questions? afarrel@juniper.net adrian@olddog.co.uk